## Slide 1: Basic Networking Concepts: LANs, WANs, and Multiplexing
Carey Williamson
Department of Computer Science
University of Calgary

## Slide 2: LANs and WANs
Networks come in many shapes and sizes
LAN: Local Area Network
  Limited geographic coverage (e.g., lab, building)
  Examples: home network, Ethernet LAN, WiFi
MAN: Metropolitan Area Network
  Size of a “city” (1-10 km or so)
WAN: Wide Area Network
  Large geographic coverage (e.g., country, planet)
  Examples: CANARIE, cellular networks, Internet
Technologies differ (capacity, distance, $$)

## Slide 3: Some Useful Analogies
Many of the concepts in computer networks are not really new, but come from other familiar areas…
Telephone network: (POTS: Plain Old Telephone System)
  Phone calls, trunk lines, toll offices, circuit-switching
Postal system: (most similar to Internet packet-switching!)
  Letters/parcels, addresses, mail carriers, post office
Highway network:
  Cars/buses, streets/highways, rush hour, collisions
Broadcast TV:
  Channels, stations, TVs, streaming (live/stored)

## Slide 4: Communications Networks
Historically, there have been two different philosophies guiding the design, operation, and evolution of communication networks
  the “telco” view (i.e., telecommunications networks to support voice telephony and other types of services, such as fax, dialup modems, etc.)
  the “data networking” view (i.e., the Internet)
While the two approaches share some similar goals and challenges (e.g., scale, geography, heterogeneity), they have quite different underlying assumptions

## Slide 5: Telco Networks (1 of 2)
Over 100 years old
Circuit-switched network
Designed for transmission of human voice
Twisted pair copper wire for residential access
  “cheap”, adequate bandwidth, easy to handle...
Aggregation of multiple calls at toll office for multiplexing/demultiplexing using TDM
Low bandwidth required per call (e.g., 64 kbps)
Fixed bandwidth required per call

## Slide 6: Telco Networks (2 of 2)
Call routing and circuit allocation decided once per call at time of call arrival
End-to-end path allocation, with dedicated circuit (reserved bandwidth) per active call
All bits travel same path; stay in same order
Call state information crucial in network switches
Busy signal if no path possible (blocking <= 2%)
Billing model based on time used (in minutes)
Single class of service; high reliability (99.99%)
Additional services: faxes, modems, mobility, ...

## Slide 7: The Internet (1 of 2)
About 50 years old
Packet-switched network
Designed for transmission of data
Variable-size packets permitted
Wide range of access technologies
Wide range of user and application behaviour
Bursty, variable bandwidth required by apps
Aggregation of traffic at routers/switches
Transmission links shared on stat mux basis

## Slide 8: The Internet (2 of 2)
Connection-less network layer protocol (IP)
“Best effort” datagram delivery model
Packet routing decided on a per-packet basis
No end-to-end path allocation; no reserved bandwidth per active call
Packets can travel any path; packets can be delayed, lost, duplicated, re-ordered
Minimal state info in network switches
Single class of service
Billing model? (hours? pkts? bytes? bandwidth?)

## Slide 9: Time Division Multiplexing (TDM)
Static channel allocation mechanism
Divides a fixed resource among N concurrent users
Done in the time domain (i.e., turn-taking, time slots)
Give each user all of the channel part of the time
Examples:
  Classroom scheduling; traffic lights; daily TV programs
  T1 digital transmission standard (1.5 Mbps)
Very efficient if N is fixed and all N users are active
Very inefficient for bursty and unpredictable traffic

## Slide 10: Frequency Division Multiplexing (FDM)
Static channel allocation mechanism
Divides a fixed resource among N concurrent users
Done in the frequency domain (i.e., Hertz) (Hz)
Give each user part of the channel all of the time
Examples:
  Radio stations; TV channels; WiFi channels
  CRTC regulation of wireless/cellular technologies
Very efficient if N is fixed and all N users are active
Very inefficient for bursty and unpredictable traffic

## Slide 11: Statistical Multiplexing (Stat Mux)
Flexible (dynamic) channel allocation mechanism
Shares a fixed resource among N concurrent users
Done dynamically on a packet-by-packet basis
Give each user the channel when they need it
Hope they don’t all need it at exactly same time!
Examples:
  Cars on city streets; letters sent via Canada Post
  Internet packets on ISP link
Very efficient for bursty and unpredictable traffic, even if N is unknown or highly dynamic

## Slide 12: Summary
There are several key concepts that underly many of the computer networks that we will talk about:
  Network edge: end system devices, access links, LAN
  Network core: aggregation, switching, multiplexing, WAN
Many of the design principles will be familiar to you from other human “communication systems”
An “internetwork” is a “network of networks”
“The Internet” is a massive global internetwork
Protocols are the glue for putting these together