## Slide 1: Networking Basics: A Review
Carey Williamson
Department of Computer Science
University of Calgary

## Slide 2: Communications Networks
Historically, there have been two different philosophies guiding the design, operation, and evolution of communication networks
  the “telco” view (i.e., telecommunications networks to support voice telephony and other emerging services, such as fax, data, location, etc.)
  the “data networking” view (i.e., the Internet)
While the two approaches share some similar goals and challenges (e.g., scale, geography, heterogeneity), they often have quite different underlying assumptions

## Slide 3: Telco Networks (1 of 2)
Over 100 years old
Circuit-switched network
Designed for transmission of human voice
Twisted pair copper wire for residential access
  “cheap”, adequate bandwidth, easy to handle...
Aggregation of multiple calls at toll office for multiplexing/demultiplexing using TDM
Low bandwidth required per call (e.g., 64 Kbps)
Fixed bandwidth required per call

## Slide 4: Telco Networks (2 of 2)
Call routing and circuit allocation decided once per call at time of call arrival
End to end path allocation, with dedicated circuit (reserved bandwidth) per active call
All bits travel same path; stay in same order
Call state information crucial in network switches
Busy signal if no path possible (blocking <= 2%)
Billing model based on time used (in minutes)
Single class of service; high reliability (99.99%)
New services: faxes, modems, mobility, ...

## Slide 5: The Internet (1 of 2)
About 50 years old
Packet-switched network
Variable size packets permitted
Designed for transmission of data
Wide range of access technologies
Wide range of user and application behaviour
Bursty, variable bandwidth required per call
Aggregation of traffic at routers/switches
Transmission links shared on stat mux basis

## Slide 6: The Internet (2 of 2)
Connection-less network layer protocol (IP)
“Best effort” datagram delivery model
Packet routing decided on a per packet basis
No end to end path allocation; no reserved bandwidth per active call
Packets can travel any path; packets can be delayed, lost, duplicated, re-ordered
Minimal state info in network switches
Single class of service
Billing model? (hours? pkts? bytes? bandwidth?)

## Slide 7: Internet Protocol Stack
Application: supporting network applications and end-user services
  FTP, SMTP, HTTP, DNS, NTP
Transport: end to end data transfer
  TCP, UDP
Network: routing of datagrams from source to destination
  IPv4, IPv6, BGP, RIP, routing protocols
Data Link: hop by hop frames, channel access, flow/error control
  PPP, Ethernet, IEEE 802.11b
Physical: raw transmission of bits
Application
Transport
Network
Data Link
Physical
001101011...

## Slide 8: Internet Protocol Stack
Application
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
Core
Network

## Slide 9: Internet Protocol Stack
Application
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
Router

## Slide 10: Internet Protocol Stack
Application
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
Switch