## Slide 1: CPSC 641: Network Measurement
Carey Williamson
Department of Computer Science
University of Calgary

## Slide 2: Network Traffic Measurement
A focus of networking research for 30+ years
Collect data or packet traces showing packet activity on the network for different applications
Study, analyze, characterize Internet traffic
Goals:
  Understand the basic methodologies used
  Understand the key measurement results to date

## Slide 3: Why Network Traffic Measurement?
Understand the traffic on existing networks
Develop models of traffic for future networks
Useful for simulations, capacity planning studies

## Slide 4: Measurement Environments
Local Area Networks (LAN’s)
  e.g., Ethernet LANs
Wide Area Networks (WAN’s)
  e.g., the Internet
Wireless LANs
Cellular Networks

## Slide 5: Requirements
Network measurement requires hardware or software measurement facilities that attach directly to network
Allows you to observe all packet traffic on the network, or to filter it to collect only the traffic of interest
Assumes broadcast-based network technology, superuser permission

## Slide 6: Measurement Tools (1 of 3)
Can be classified into hardware and software measurement tools
Hardware: specialized equipment
  Examples: HP 4972 LAN Analyzer, DataGeneral Network Sniffer, NavTel InterWatch 95000, others...
Software: special software tools
  Examples: tcpdump, ethereal, wireshark, SNMP, others...

## Slide 7: Measurement Tools (2 of 3)
Measurement tools can also be classified as active or passive
Active: the monitoring tool generates traffic of its own during data collection (e.g., ping, traceroute)
Passive: the monitoring tool is passive, observing and recording traffic info, while generating none of its own (e.g., tcpdump, wireshark, airopeek)

## Slide 8: Measurement Tools (3 of 3)
Measurement tools can also be classified as real-time or non-real-time
Real-time: collects traffic data as it happens, and may even be able to display traffic info as it happens, for real-time traffic management
Non-real-time: collected traffic data may only be a subset (sample) of the total traffic, and is analyzed off-line (later), for detailed analysis

## Slide 9: Potential Uses of Tools (1 of 4)
Protocol debugging
  Network debugging and troubleshooting
  Changing network configuration
  Designing, testing new protocols
  Designing, testing new applications
  Detecting network weirdness: broadcast storms, routing loops, etc.

## Slide 10: Potential Uses of Tools (2 of 4)
Performance evaluation of protocols and applications
  How protocol/application is being used
  How well it works
  How to design it better

## Slide 11: Potential Uses of Tools (3 of 4)
Workload characterization
  What traffic is generated
  Packet size distribution
  Packet arrival process
  Burstiness
  Important in the design of networks, applications, interconnection devices, congestion control algorithms, etc.

## Slide 12: Potential Uses of Tools (4 of 4)
Workload modeling
  Construct synthetic workload models that concisely capture the salient characteristics of actual network traffic
  Use as representative, reproducible, flexible, controllable workload models for simulations, capacity planning studies, etc.

## Slide 13: Classic References
Raj Jain, ‘‘Packet Trains”, 1986
Cheriton and Williamson, “VMTP”, 1987
Chiu and Sudama, “DECNET Protocols”, 1988
Gusella, “Diskless Workstations”, 1990
Caceres et al, “Wide Area TCP/IP Traffic”, 1991
Paxson, “Measurements and Models of Wide Area TCP Traffic”, 1991
Leland et al, “Network Traffic Self-Similarity”, 1993
Garrett, Willinger, “VBR Video”, 1994
Paxson and Floyd, “Failure of Poisson Modeling”, 1994

## Slide 14: Top 10 Measurement Results
The following represents my own synopsis of the “Top 10” observations from network traffic measurement research in the last 30 years
Not an exhaustive list, but most of the highlights
For more detail, see papers (or ask!)

## Slide 15: Observation #1
The traffic model that you use is extremely important in the performance evaluation of routing, flow control, and congestion control strategies
  Have to consider application-dependent, protocol-dependent, and network-dependent characteristics
  The more realistic, the better
  Need to avoid the GIGO syndrome

## Slide 16: Observation #2
Characterizing aggregate network traffic is hard
  Lots of (diverse and ever-changing) applications
  Any measurement study provides just a snapshot in time: traffic mix, protocols, applications, network configuration, technology, and users change with time

## Slide 17: Observation #3
Packet arrival process is not Poisson
  Packets travel in trains
  Packets travel in tandems
  Packets get clumped together (e.g., ACK compression)
  Interarrival times are not exponential
  Interarrival times are not independent

## Slide 18: Observation #4
Packet traffic is bursty
  Average utilization may be very low
  Peak utilization can be very high
  Depends on what interval you use!!
  Traffic may be self-similar: bursts exist across a wide range of time scales
  Defining burstiness (precisely) is difficult

## Slide 19: Observation #5
Traffic is non-uniformly distributed amongst the hosts on the network
  Example: 10% of the hosts account for 90% of the traffic (or 20-80 rule, as in the “Pareto principle”)
  Why? Clients versus servers, geographic reasons, popular Web sites, trending events, flash crowds, etc.

## Slide 20: Observation #6
Network traffic exhibits ‘‘locality’’ effects
  Pattern is far from random
  Temporal locality
  Spatial locality
  Persistence and concentration
  True at host level, at router level, at application level

## Slide 21: Observation #7
Well over 90% of the byte and packet traffic on most networks is TCP/IP
  By far the most prevalent
  Often as high as 95-99%
  Most studies focus only on TCP/IP for this reason

## Slide 22: Observation #8
Most conversations are short
  Example: 90% of bulk data transfers send less than 10 kilobytes of data
  Example: 50% of interactive connections last less than 90 seconds
  Distributions may be ‘‘heavy tailed’’ (i.e., extreme values may skew the mean and/or the distribution)

## Slide 23: Observation #9
Traffic is bidirectional
  Data usually flows both ways
  Not just ACKs in the reverse direction
  Usually asymmetric bandwidth though
  Pretty much what you would expect from the TCP/IP traffic for most applications

## Slide 24: Observation #10
Packet size distribution is bimodal
  Lots of small packets for interactive traffic and acknowledgements (ACKs)
  Lots of large packets for bulk data file transfer type applications
  Very few in between sizes

## Slide 25: Summary
There has been lots of interesting network measurement work in the last 30 years
We will take a look at some of it soon
LAN and WAN traffic measurements
Network traffic self-similarity