## Slide 1: Queueing Theory
Carey Williamson
Department of Computer Science
University of Calgary

## Slide 2: Outline
Plan:
  Introduce basics of Queueing Theory
  Define notation and terminology used
  Discuss properties of queueing models
  Show examples of queueing analysis:
    M/M/1 queue
    Variations on the M/G/1 queue
    Open queueing network models
    Closed queueing network models

## Slide 3: Queueing Theory Basics
Queueing theory provides a very general framework for modeling systems in which customers must line up (queue) for service (use of resource)
  Banks (tellers)
  Restaurants (tables and seats)
  Computer systems (CPU, disk I/O)
  Networks (Web server, router, WLAN)

## Slide 4: Queue-based Models
Queueing model represents:
  Arrival of jobs (customers) into system
  Service time requirements of jobs
  Waiting of jobs for service
  Departures of jobs from the system
Typical diagram:
Customer
Arrivals
Departures
Buffer
Server

## Slide 5: Why Queue-based Models?
In many cases, the use of a queueing model provides a quantitative way to assess system performance
  Expected waiting time for service
  Number of buffers required to limit loss of customers
  Response time (e.g., Web page download time)
  Throughput (e.g., job completions per second)
Reveals key system insights (properties)
Often with efficient, closed-form calculation

## Slide 6: Caveats and Assumptions
In many cases, using a queueing model has the following implicit underlying assumptions:
  Poisson arrival process
  Exponential service time distribution
  Single server
  Infinite capacity queue
  First-Come-First-Serve (FCFS) discipline (a.k.a. FIFO)
  Note: important role of memoryless property!

## Slide 7: Advanced Queueing Models
There is a tonne of published work on variations of the basic model:
  Correlated arrival processes
  General (G) service time distributions
  Multiple servers
  Vacationing servers
  Finite capacity systems
  Other scheduling disciplines (non-FIFO)
We will start with the basics!

## Slide 8: Queue Notation
Queues are concisely described using the Kendall notation, which specifies:
  Arrival process for jobs {M, D, G, …}
  Service time distribution {M, D, G, …}
  Number of servers {1, n}
  Storage capacity (buffers) {B, infinite}
  Service discipline {FIFO, PS, SRPT, …}
Examples: M/M/1, M/G/1, M/M/c/c

## Slide 9: The M/M/1 Queue
Assumes Poisson arrival process, exponential service times, single server, FCFS service discipline, infinite capacity for storage, with no loss
Notation: M/M/1
  Markovian arrival process (Poisson)
  Markovian service times (exponential)
  Single server (FCFS, infinite capacity)

## Slide 10: The M/M/1 Queue (cont’d)
Arrival rate: λ (e.g., customers/sec)
  Inter-arrival times are exponentially distributed and independent with mean 1 / λ
Service rate: μ (e.g., customers/sec)
  Service times are exponentially distributed and independent with mean 1 / μ
System load: ρ = λ / μ
  0 ≤ ρ ≤ 1 (also known as utilization factor)
Stability criterion: ρ < 1 (single server systems)

## Slide 11: Queue Performance Metrics
N: Avg number of customers in system as a whole, including any in service
Q: Avg number of customers in the queue (only), excluding any in service
W: Average waiting time in queue (only)
T: Avg time spent in system as a whole, including waiting time plus service time
Note: Little’s Law: N = λ T

## Slide 12: M/M/1 Queue Results
Average number of customers in the system: N = ρ / (1 – ρ)
Variance: Var(N) = ρ / (1 - ρ)2
Waiting time: W = ρ / (μ (1 – ρ))
Time in system: T = 1 / (μ (1 – ρ))

## Slide 13: The M/D/1 Queue
Assumes Poisson arrival process, deterministic (constant) service times, single server, FCFS service discipline, infinite capacity for storage, no loss
Notation: M/D/1
  Markovian arrival process (Poisson)
  Deterministic service times (constant)
  Single server (FCFS, infinite capacity)

## Slide 14: M/D/1 Queue Results
Average number of customers: Q = ρ/(1 – ρ) – ρ2 / (2 (1 - ρ))
Waiting time: W = x ρ / (2 (1 – ρ)) where x is the mean service time
Note that lower variance in service time means less queueing occurs 

## Slide 15: The M/G/1 Queue
Assumes Poisson arrival process, general service times, single server, FCFS service discipline, infinite capacity for storage, with no loss
Notation: M/G/1
  Markovian arrival process (Poisson)
  General service times (must specify F(x))
  Single server (FCFS, infinite capacity)

## Slide 16: M/G/1 Queue Results
Average number of customers:
Q = ρ + ρ2 (1 + C2) / (2 (1 - ρ)) where C is the Coefficient of Variation (CoV) for the service-time distribution F(x)
Waiting time:
  W = x ρ (1 + C2 ) / (2 (1 – ρ)) where x is the mean service time from distribution F(x)
Note that variance of the service time distn could be higher or lower than for exponential distn!

## Slide 17: The G/G/1 Queue
Assumes general arrival process, general service times, single server, FCFS service discipline, infinite capacity for storage, with no loss
Notation: G/G/1
  General arrival process (specify G(x))
  General service times (must specify F(x))
  Single server (FCFS, infinite capacity)

## Slide 18: Queueing Network Models
So far we have been talking about a queue in isolation
In a queueing network model, there can be multiple queues, connected in series or in parallel (e.g., CPU, disk, teller)
Two versions:
  Open queueing network models
  Closed queueing network models

## Slide 19: Open Queueing Network Models
Assumes that arrivals occur externally from outside the system
Infinite population, with a fixed arrival rate, regardless of how many are in the system
Unbounded number of customers are permitted within the system
Departures leave the system (forever)

## Slide 20: Closed Queueing Network Models
Assumes that there is a finite number of customers, in a self-contained world
Finite population; arrival rate varies depending on how many and where
Fixed number of customers (N) that recirculate in the system (forever)
Can be analyzed using Mean Value Analysis (MVA), recurrence relations, and balance equations