## Slide 1: Simulation
Carey Williamson
Department of Computer Science
University of Calgary

## Slide 2: Outline
Plan:
  Introduce basics of simulation modeling
  Define terminology and methods used
  Introduce simulation paradigms
    Monte Carlo simulation
    Time-driven simulation
    Event-driven simulation
  Technical issues for simulations
    Random number generation
    Statistical inference

## Slide 3: Monte Carlo Simulation
Estimating an answer to some difficult problem using numerical approximation, based on random numbers
Examples: numerical integration, primality testing, WSN coverage, poker hands
Suited to stochastic problems in which probabilistic answers are acceptable
Might be one-sided answers (e.g., prime)
Can bound probability to some epsilon
There is (usually) no notion of time at all

## Slide 4: Time-Driven Simulation
Time advances in fixed size steps
Time step = smallest unit in model
Check each entity to see if state changes
Well-suited to continuous systems
  e.g., river flow, factory floor automation
Granularity issue:
  Too small: slow execution for model
  Too large: miss important state changes

## Slide 5: Event-Driven Simulation (1 of 2)
Discrete-event simulation (DES)
System is modeled as a set of entities that affect each other via events (messages)
Each entity can have a set of states
Events happen at specific points in time (continuous or discrete), and trigger state changes in the system
Very general technique, well-suited to modeling discrete systems (e.g, queues)

## Slide 6: Event-Driven Simulation (2 of 2)
Typical implementation involves an event list, ordered by time
Process events in (non-decreasing) timestamp order, with seed event at t=0
Each event can trigger 0 or more events
  Zero: “dead end” event
  One: “sustaining” event
  More than one: “triggering” event
Simulation ends when event list is null, or desired time duration has elapsed

## Slide 7: Summary
Simulation methods offer a range of general-purpose approaches for performance eval
Simulation modeler must determine the appropriate aspects of system to model
“The hardest part about simulation is deciding what not to model.” - M. Lavigne
Many technical issues: RNG, validation, statistical inference, efficiency
We will look at some examples soon