## Slide 1: WiFi Networks: IEEE 802.11b Wireless LANs
Carey Williamson
Department of Computer Science
University of Calgary

## Slide 2: Background (1 of 2)
In many respects, the IEEE 802.11b wireless LAN (WLAN) standard is similar to that for classic IEEE 802.3 (Ethernet) LANs
Similarities:
  LAN with limited geographic coverage
  multiple stations, with 48-bit MAC addresses
  shared transmission medium (broadcast technology)
  CSMA-based Medium Access Control protocol
  comparable data rates (11 Mbps vs 10 Mbps)

## Slide 3: Background (2 of 2)
But there are also many distinct differences:
  wireless (air interface) versus wired (coax)
  wireless propagation environment (multipath)
  higher error rate due to interference, etc.
  successful frames are ACKed by receiver
  mobile stations versus fixed stations
  half-duplex versus full-duplex operation
  “hidden node” and “exposed node” problems
  potential asymmetries of links
  CSMA/CA versus CSMA/CD
  multiple data transmission rates (1, 2, 5.5, 11)

## Slide 4: Some WiFi Features
Infrastructure mode vs “ad hoc” mode
Access Point (AP) sends “beacon frames”
  Mobiles choose AP based on signal strength
Multiple channel access protocols supported
  CSMA/CA (DCF); PCF; RTS/CTS
MAC-layer can provide error control, retransmission, rate adaptation, etc.
Direct Sequence Spread Spectrum (DSSS)
  signal spread across 14 22-MHz channels

## Slide 5: Where Does Wireless RF Live?
902-928 MHz
2400-2483.5 MHz
5725-5850 MHz
802.11/802.11b,g
802.11a
Bluetooth
Cordless Phones
Home RF
Baby Monitors
Microwave Ovens
Old Wireless
ISM (Industrial, Scientific, Medical) band

## Slide 6
Telnet, FTP, Email, Web, etc.
IP, ICMP, IPX
TCP, UDP
Logical Link Control - 802.2
(Interface to the upper layer protocols)
MAC
802.3, 802.5, 802.11
Physical Layer Convergence Protocol
LAN: 10BaseT, 10Base2, 10BaseFL
WLAN: FHSS, DSSS, IR
Application
Presentation
Session
Transport
Network
Data Link
Physical
Wireless lives at
Layers 1 & 2
only!
Protocol Stack View

## Slide 7
11 Mbps bandwidth
“shared” by all devices
in the Cell!
Access Point coverage
area is called a “Cell”
Range per Access Point is 100m
Access Point Channel 6 ESSID: NAI
In Canada/US, there are eleven 802.11 channels
Only channels 1, 6 and 11 are non-overlapping
Computers can roam between cells
Wireless Cells

## Slide 8
1
6
11
1
1
11
Multiple Wireless APs

## Slide 9
Carrier Sense Multiple Access with Collision Avoidance
Device wanting to transmit senses the medium (Air)
If medium is busy - defers
If medium is free for certain period (DIFS) - transmits
How CSMA-CA works:
Latency can increase if “air” is very busy! Device
has hard time finding “open air” to send frame!
DIFS - Distributed Inter-Frame Space (approx 128 µs)
Medium Access Control (MAC)

## Slide 10
SIFS - Short Inter-Frame Space (approx 28 µs)
Every frame is acked - except broadcast and multicast!
“Air” is free
for DIFS time
period
Receive ACK
that frame was
received intact!
send frame
source
dest
others
DIFS
SIFS
All other devices
must defer while “air” is busy
data
ack
NAV: defer access
MAC Protocol (Cont’d)

## Slide 11: MAC-Layer Retransmission
If no ACK received “right away”, then the sender retransmits the frame again at the MAC layer
  indicates frame (or ACK) was lost/corrupted
  very short timeout (e.g., 1 msec)
  exponential backoff (doubling) if repeated loss
Typically recovers before TCP would notice
Max retransmission limit (e.g., 8)
May do MAC-layer rate adaptation or frame fragmentation if channel error rate is high

## Slide 12: Other MAC Protocols Supported
Point Coordination Function (PCF)
  AP polls stations in turn to see if frames to send
  useful for real-time traffic
Request-To-Send/Clear-To-Send (RTS/CTS)
  reservation-based approach (ask permission)
  useful for very large frames
  useful for solving the “hidden node” problem
  request asks for clearance (permission) to send
  request also indicates time required for transmit

## Slide 13: Frame Formats
Two frame formats available:
  long preamble
  short preamble
Configuration option for NIC and AP
Variable-size frames (max 2312 data bytes)
16-bit Cyclic Redundancy Code (CRC) for error checking of frames

## Slide 14
Long Preamble = 144 bits
Interoperable with older 802.11 devices
Entire Preamble and 48 bit PLCP Header sent at 1 Mbps
128 bit Preamble
(Long)
16 bit
Start
Frame
Delimiter
Signal Speed
1,2,5.5,11
Mbps
Service
(unused)
Length
of
Payload
16 bit
CRC
Payload
0-2312 bytes
Transmitted at 1 Mbps
Transmitted at X Mbps
Frame Format (Long Preamble)

## Slide 15
Short Preamble = 72 bits
Preamble transmitted at 1 Mbps
PLCP Header transmitted at 2 Mbps
more efficient than long preamble
56 bit
Preamble
Payload
0-2312 bytes
Transmitted
at
1 Mbps
16 bit
Start
Frame
Delimiter
Signal Speed
1,2,5.5,11
Mbps
Service
(unused)
Length
of
Payload
16 bit
CRC
Transmitted
at
2 Mbps
Transmitted
at
X Mbps
Frame Format (Short Preamble)

## Slide 16: Even More Features
Power Management
  mobile nodes can “sleep” to save power
  AP will buffer frames until client requests them
  AP can use virtual bitmap field in beacons to indicate which stations have data waiting
Security
  Wired Equivalent Privacy (WEP)
  not very secure at all!

## Slide 17: Summary
IEEE 802.11b (WiFi) is a wireless LAN technology that is rapidly growing in popularity
Convenient, inexpensive, easy to use
Growing number of “hot spots” everywhere
  airports, hotels, bookstores, Starbucks, etc
Many deployments now have IEEE 802.11g (54 Mbps) or IEEE 802.11a (also 54 Mbps)
Some deployments have IEEE 802.11n (> 100 Mbps)
U of C WLAN has about 1000 WiFi Access Points (APs)